## Slide 1
Team 05 - Caffeinator
Start
Localize
Travel To Waypoint
Arrived at Destination?
No
Yes
Approaching Obstacle?
No
Obstacle Avoidance
Localize
Yes
Launch Projectiles
Travel to Starting Position
End
Software
Flow Chart
Advanced Ultrasonic Localization
Caffeinator quickly sweeps its
surrounding and detects for the
closest distance to wall to approximate
its current position using Ultrasonic Sensor.
Accurate Light Localizer
Next, the robot travels to closest intersection
and rotates 360 degreesto detect the 4 grid
lines using light sensor for an accurate
localization of its current position.
The objective of this project is to develop an autonomous robot using the Lego Mindstorms Kits. This robot needs to be able to localize anywhere within the start area. It will then travel to the shooting area while avoiding obstacles and shoot at 2 targets with 3 ping-pong balls each. After shooting, it must return to center of the start area (0,0) and face the north.
Objective
Hardware & Software
Competition Floor
(0,0)
1
2
3
4
5
6
7
8
9
Obstacles: 30cm cubes
Area 2, 3, 4, 7: Mapped Obstacles
Small Tile: 30cm x 30cm
Obstacles: 30cm x 30cm x 30cm
Target Radius: 7.5cm
Area 5, 6, 8: Unmapped Obstacles
Built with LEGO Mindstorm Kits and designed in a small, solid and compact structure, Caffeinator is able to accomplish some fantastic tasks by the application of engineering principles.
By using the gravity force, the ping-pong balls load automatically one after the other through a cylindrical tube attached to the robot.
By using the rotational force of a LEGO motor, the sticks in dark gray will hit the ball in the resting zone, resulting the launching of the projectile.
Safe Obstacle Avoidance Full 180 degrees coverage
20 cm
Projectile Range: 150 +/- 5 cm
3 Ultrasonic Sensors
1 Light Sensor
2 Motor for flexible Navigation and Odometry
86%
Documentation Hardware Software Testing
Task Distributions
Team Members: Eric Vuong – Project Manager / Software
Gwen Pang - Documenter Yu Chen Xu – Hardware Manager Adrian Pan – Software Manager
James Fuh – Software
Yutian Zheng - Hardware
310 used /360 alloted hours